# University Racing Eindhoven & URE05e

University Racing Eindhoven:

- Studenten raceteam van 60 studenten

- Studenten afkomstig van allerlei opleidingen (werktuigbouwkunde, electrical engineering, technische bedrijfskunde, informatica)

- Deelnemer aan Formula Student

- Formula Student is internationale universiteitencompetitie met zo’n 450 deelnemers

- Formula Student races op Silverstone en Hockenheimring

- URE doet als eerste mee aan nieuwe klasse in Formula Student: Formula Student electric

- Auto van URE is de URE05e

- Kenmerken van de auto staan in onderstaande tabel:

| Chassis Front | Full Carbon fiber monocoque |
| --- | --- |
| Chassis back | Steel tubular space frame |
| Weight | 250 kg (wet weight) |
| Max. power | 60 kW |
| Max.current | 930 A |
| Max. voltage | 110 V |
| Max. torque | 160 Nm |
| Max. rpm | 6.000 rpm |
| Top speed | 100 km/h |
| Battery cells | 78 Li-Ion Polymer |
| Motors | 2 Agni 119R Motors |
| Motor controllers | 2 Kelly Controllers |
| Differential | Active electronic differential |
| Rims | 13” Aluminium Keizer Wheels with magnesium center |
| Tires | 20.5×7-13 R25B Hoosier |
| Suspension | Full Multi link |
| Brakes | Custom designed brake discs |
| Options | Traction control |
| Track width front | Full 1225 mm |
| Track width rear | 1175 mm |
| wheelbase | 1600 mm |
| Overall length | 2745 mm |
| Overall width | 1334 mm |
| Overall height | 1062 mm |

Contactgegevens University Racing Eindhoven:

Joni Driessen

Operations & Finance Manager

University Racing Eindhoven

Tel: 040 247 35 99

Mob: 06 100 942 94

Fax: 040 243 49 70

E-mail: j.p.c.driessen@student.tue.nl

Web: www.universityracing.nl